| Shear Wall Schedule – Dent Residence |
| --- |
|  | WALL INFORMATION | FASTENERS (Where Applicable) |
| WALL | WALL SHEATHING | EDGE NAILING | FIELD NAILING | SILL PLATE | RIM JOIST | FOUNDATION ANCHORS |
| SW - 6 | 1/2" O.S.B. on one side of wall | 8d @ 6" o.c. | 8d @ 12" o.c. | 16d @ 6" o.c. | 16d TOENAILS @ 4" o.c. | 1/2" x 10" A.B. @ 48" o.c. |
| SW - 4 | 1/2" O.S.B. on one side of wall | 8d @ 4" o.c. | 8d @ 12" o.c. | 16d @ 4" o.c. | 16d TOENAILS @ 3" o.c. | 1/2" x 10" A.B. @ 30" o.c. |

SCHEDULE NOTES:

- All exterior framed walls not designated with a wall label shall be sheathed and anchored according to the requirements of shear wall 6.

- Studs shall be spaced at 16” o.c. maximum (plywood may be installed either vertically or horizontally)

- All shear panels are to be continuous between horizontal diaphragms (roof to floor, floor to floor, floor to foundation)

- All framed shear walls shall be blocked at all panel edges.